## Slide 1
Air Cooling system of the ALICE LS3 ITS upgrade
Anuj Dabeesingh
Summer student 2019
EP-DT
Supervisors:
Corrado Gargiulo
Elisa Laudi

## Slide 2
Introduction
High School ‘A’ Levels in Maths, Chemistry & Physics 2007, Mauritius.
Bachelor's degree Jun 2011 – Sept 2014 (Brunel University, UK)
Master degree Sept 2017-Oct 2019 in Advanced Mechanical Engineering (Cranfield University, UK)
Summer student at CERN July- Aug 2019

## Slide 3
The Alice detector – cooling system (ITS2)
ALICE:
It is one of LHC’s four detectors
Analysis of particle collisions at the quark-gluon plasma phase
Comprehensive study of hadrons, electrons, muons, photons during heavy nuclei collisions.
ALICE Central detector is an Inner Tracking System ITS being upgraded for LS2, based on monolithic pixel chip sensors
LS2 Upgrade is targeted for 2020
LS3 Upgrade 2024 - 2026
ITS Water cooling:
Removes 14.8 kW of thermal energy
Water out ranging from 18 C to 23 C
N.48 loops
N.4 controlled manifolds
ITS Air cooling:
150m3/h of air for heat exchange
Outlet temperature is 20 C
35% of humidity is processed
ALICE
Inner Tracking System (ITS2)
ALICE Cavern

## Slide 4
ITS3 Stitching & Bending
chip size is traditionally limited by CMOS manufacturing (“reticle size”)
new option: stitching, i.e. aligned exposures of given parts of a reticle to produce a larger circuit
on a width of a 300 mm wafer (available in 65 nm technology node), a single chip ﬁts a full half-layer
Courtesy: R. Turchetta, Rutherford Appleton Laboratory
Principle of photolithography
Bending Si wafers + circuits is possible!
Radii much smaller than ALICE needs are obtained
Circuit-speciﬁc R&D is needed
R&D contact with IZM (Fraunhofer) has started
Investigating options to start with existing
ALPIDE chips + wafers
Chipworks: 30µm-thick RF-SOI CMOS

## Slide 5
ITS3 Interface and connectivity
Possible layout based on air-cooling/ peripheral cooling
Sensors hold in place with low-density carbon foam
Fixation into the experiment by surrounding support structure, as well as at both ends
Cooling at the extremities (chip peripheries)

## Slide 6
R&D Plan
Thermal characterisation
Test the exchange of heat from the carbon foam to the air
Vary the carbon foam density
Test the different geometries
Use different air velocities
Simulation of the model on CFD
Build a full setup wind tunnel test rig for design validation
Structural characterisation
Build a full CAD model of the test system
Perform FEA at different air speeds to test for resonance
Perform wind tunnel test and vibration test on shaker for design validation

## Slide 7
Materials & Processes
Carbon foam used as radiator in detector GAS cooling application
It is possible to obtain convective heat transfer enhancement by bonding a layer of foam to a solid substrate and allowing air to ﬂow across the foam surface.
The high eﬀective conductivity ensures that the layer of foam readily entrains heat out of the solid substrate to be swept away by passing ﬂuid.
Convective heat transfer enhancement then occurs in two ways: ﬁrst due to the roughness of the exposed surface, and second due to the additional surface area exposure to ﬂuid that inﬁltrates the foam.
Scanning electron micrograph of the carbon foam surface
Scanning electron micrograph of the carbon foam surface of a single pore.
Surface to volume ratio as large as 5000 m -1 to 50000 m-1
Graphite foam heat sinks (a) block, (b) stagger, (c) baffle and (d) zigzag configurations.
  The most important problem facing the graphite foam heat exchanger is the pressure drop. In order to reduce the pressure drop, it is important to adopt an appropriate configuration of the graphite foams.

## Slide 8: Carbon foam properties

## Slide 9: CFD Simulations- Parameters
Density of air – 1.2 kg/m3
3D Hex Mesh
Models - Realizable k‐ε (2 eqn)
Velocity Specification Method: Magnitude and Direction
Velocity Magnitude: 2.2m/s
X‐Component: 1
Y‐Component: 0
Z‐Component: 0
Turbulence Intensity: 5%
Turbulent Viscosity Ratio: 10
Area – 1 m2
Length – 1m
Carbon foam block
Outer boundary air flow volume
2.2m/s
CFD first step analysis goal is to simulate heat exchange between Carbon foam and air
A simple model is being used in this first phase to tune the different parameter and the Carbon foam geometry.
Mesh optimization
Ongoing simulation to analyse results acc. To different parameters: Porosity, Thermal conductivity, Stiffness, Density & Geometry

## Slide 10: Appendix – ITS2
Inner Barrel (IB) layers 0 to 2
Outer barrel (OB) layers 3 to 6
Space Frame – structure of C.fibre for support
Cold Plate – A sheet of high thermal conductivity
Hybrid Integrated Circuit (HIC) – Assembly of a polyimide Flexible Printed Circuit (FPC) bonded with pixel chips and passive components

## Slide 11: Appendix – ITS2 vs ITS3
ITS2 | ITS3
Sensor @ 50 micrometers | CMOS manufacturing @ 30 micrometers
Water & Air cooling | Air cooling only
IB (0 to 2),OB Middle (3 & 4), Outer (5 &6) | New IB & OB(3 to 6) of ITS2

## Slide 12: Appendix – ITS3 characteristics